## Slide 1: Domain Generalization for CSI Compression
Cristian J. Vaca-Rubio, PhD.

## Slide 2: EVERYTHING IN 2 MINUTES
Data understanding  Angular vs. Delay Domain: Which one matters
ML insights  How does domain shift disrupt learning?
Generalization  How can we fight back against domain shift?
2/30
the most?

## Slide 3: Data understanding
3/30

## Slide 4: Dataset Overview
Dataset: COST2100 (Indoor & Outdoor), preprocess per CSINet
  Indoor  picocellular scenario at 5.3 GHz band, 20x20 m scenario
  Outdoor  rural scenario at the 300 MHz band, 400x400 m scenario
  Uniform Linear Array (ULA) with 32 antennas and 1024 subcarriers
CSI in truncated delay–angle (32×32) domain after 2D DFT
Values normalized to bounded range [0, 1]
Comparing Indoor vs Outdoor CSI structure and understanding their main differences
4/30

## Slide 5: Why Angles Matter?
Indoor CSI (5.3 GHz Picocell)
  High angular sparsity
  Dominant LOS and small spatial spreads
Outdoor Rural CSI (300 MHz)
  Broad angular distribution
  Widely separated scattering clusters and diffraction-induced angular diversity
Indoor vs Outdoor = angular distribution mismatch
5/30

## Slide 6: Does Delay Matter as Much?
Early delay taps (0–4) concentrate most of the power
  LOS (indoors)
  Strong NLOS components such as diffraction and ground reflections (outdoor)
Indoor and outdoor channels exhibit very similar decay patterns
Outdoor samples retain slightly more late-tap activity
Delay statistics barely shift
6/30

## Slide 7: Heatmap Examples
Indoor CSI exhibits highly localized structure
  Energy concentrated in just 1–2 angle bins and a few delay taps
  Indoor samples display very low variability
7/30
Outdoor CSI shows multiple clusters distributed across both delay and angle
  Less focused in angle
  Outdoor samples vary significantly
Indoor↔Outdoor structural changes cause a strong domain shift that ML models cannot generalize across

## Slide 8: Quantitative Difference Indoor & Outdoor CSI
Angular statistics (spread, sparsity, and KL divergence) show a strong structural domain shift
8/30

## Slide 9: Role of Sparsity in CSI Compression & Generalization
Sparsity helps in-domain reconstruction
  Indoor CSI is highly structured and consistent → near-perfect reconstruction
  Most CSI compression methods can benefit on this sparsity
Sparsity differences hurt cross-domain generalization
  Indoor CSI is very sparse (few angles, few delays)
  Outdoor CSI is less sparse and more variable (multiple clusters, broad angles, longer delays)
Sparsity compresses, but environmental shifts break its structure
9/30

## Slide 10: ML training & insights
10/30

## Slide 11: CSINet
Reimplementation of original CSINet architecture in PyTorch
11/30

## Slide 12: Why Domain Shift Matters for CSINet?
CSINet learns a compressed latent representation of CSI
If the input distribution changes (indoor  outdoor), the encoder activates different patterns
Hypothesis  mismatch leads to:
  Poor reconstruction
  High Normalized Mean Squared Error (NMSE)
12/30

## Slide 13: Training setup
Architecture: CSINet with same parameters
Encoder dimension: 512 (ratio ¼)
Domain options:
  Train Indoor
  Train Outdoor
  Train Indoor+Outdoor
Splits given in train/val/test
Training by using the Mean Squared Error (MSE) function, similarly as CSINet
Selected model that minimizes validation loss
Early stopping mechanism implemented with 10 epochs patience
13/30

## Slide 14: Learning Curve: Indoor Training
Smooth convergence
Best validation at epoch 25
Indoor data is easy to compress (low variability, compact multipath)
No overfitting behavior
25 epochs
14/30

## Slide 15: Learning Curve: Outdoor Training
Much slower convergence
Best validation at epoch 48
Outdoor CSI has wider angular spread  harder to encode
No overfitting behavior
25 epochs
48 epochs
15/30

## Slide 16: Learning Curve: Indoor+Outdoor Training
Longer training until convergence
Best validation at epoch 71
Learns more general features
No overfitting behavior
Joint model learns a balanced latent space
25 epochs
48 epochs
71 epochs
16/30

## Slide 17: NMSE Results on Test set
  Models generalize poorly across domains
  A jointly trained-model achieves the best overall robustness:
    The model is learning a shared structure rather than overfitting to a single environment
  Indoor-only model performs great, but collapses elsewhere
  Outdoor-only model generalizes slightly better than indoor-only
17/30

## Slide 18: Generalization
18/30

## Slide 19: Replay Fine-Tuning Mechanism
Target-domain CSI
Source-domain CSI
Target-domain CSI
Source-domain CSI
19/30

## Slide 20: Replay Fine-Tuning Mechanism
Continual learning-inspired
Motivated by settings where new environments are available after initial training
  Goal: Adapt a model from a source domain Ds to a target domain Dt while preventing catastrophic forgetting on Ds
  During training a mix of samples from both the target-domain and the replay (cached) source-domain
The learning is encouraged by a combined loss
20/30

## Slide 21: Learning Curves
Standard Fine-Tuning
Replay Fine-Tuning
21/30

## Slide 22: Results on Test Set
22/30
Replay fine-tuning improves cross-domain performance while reducing catastrophic forgetting
Simple fine-tuning leads to heavy catastrophic forgetting
Outdoor-trained models generalize better because Outdoor CSI is more complex; once learned, Indoor patterns are a simpler refinement

## Slide 23: Domain-Aware Architecture
Encoder
Source domain CSI decoder
Target domain CSI decoder
Phase 1
Phase 1
Phase 2
Phase 2
ConvAdapter
Frozen Encoder + Adapter
Adapter only active in Phase 2
23/30

## Slide 24: Domain-Aware Architecture
Motivated by settings where new environments are available after initial training
  Goal: Adapt a model from a source domain Ds to a target domain Dt while preventing catastrophic forgetting on Ds
The catastrophic forgetting is prevented by an adaptive filter
Sparsity knowledge is also leveraged
ConvAdapter
Frozen Encoder (shared) + Lightweight Adapter (trainable)
Active only during target-domain adaptation (Phase 2)
24/30

## Slide 25: Intuition Behind Adaptive Filter
The encoder is frozen -> preserves performance on source domain
The adapter applies a small, low-rank residual update
This lets the model slightly change the feature space for the new domain
Without overwriting what was learned before  no catastrophic forgetting
25/30

## Slide 26: Learning Curves
26/30

## Slide 27: Results on Test Set
Domain-Aware improves cross-domain performance reducing catastrophic forgetting even further
27/30

## Slide 28: Test Set Exemplary Heatmaps
28/30
Indoors evaluation
(IndoorOutdoor)
|(OutdoorIndoor)
Outdoors evaluation
(IndoorOutdoor)
|(OutdoorIndoor)

## Slide 29: Conclusions and future work
29/30
Angular domain is the main source of domain shift
CSINet struggles to generalize across different environments
Replay finetuning mitigates catastrophic forgetting
Domain-aware with ConvAdapters further improves adaptation
Latent-invariant features through contrastive learning
Explore foundation models and transformer-based architectures
In the real world for CSI compression TX-RX are involved
  Gradients are not perfect!

## Slide 30: References
[1] Wen, C. K., Shih, W. T., & Jin, S. (2018). Deep learning for massive MIMO CSI feedback. IEEE Wireless Communications Letters, 7(5), 748-751.
[2] GitHub - sydney222/Python_CsiNet: Python code for "Deep Learning for Massive MIMO CSI Feedback“
[3] Dataset: COST2100 (used in original CSINet paper)
[4] Liu, L., Oestges, C., Poutanen, J., Haneda, K., Vainikainen, P., Quitin, F., ... & De Doncker, P. (2012). The COST 2100 MIMO channel model. IEEE Wireless Communications, 19(6), 92-99
[5] Mohsin, M. A., Umer, M., Bilal, A., Jamshed, M. A., & Cioffi, J. M. (2025). Continual Learning for Wireless Channel Prediction. arXiv preprint arXiv:2506.22471
[6] Houlsby, N., Giurgiu, A., Jastrzebski, S., Morrone, B., De Laroussilhe, Q., Gesmundo, A., ... & Gelly, S. (2019, May). Parameter-efficient transfer learning for NLP. In International conference on machine learning (pp. 2790-2799). PMLR
[7] Rebuffi, S. A., Bilen, H., & Vedaldi, A. (2017). Learning multiple visual domains with residual adapters. Advances in neural information processing systems, 30.
30/30

## Slide 31: Thank you for your attention!

## Slide 32: Backup slides

## Slide 33: Dataset Processing
Dataset and GitHub inspection (CSINet) reveal the applied normalization strategy
  CSI is already transformed into the angular–delay domain (32 × 32)
    Obtained via DFT across subcarriers (delay domain)
    And DFT across antennas (angular domain)
    This is the standard representation used in CsiNet-based compression
  CSI values are shift-normalized
    Stored as real_raw + 0.5, imag_raw + 0.5
    Ensures all stored values are within [0, 1]
  For analysis, we denormalize by subtracting 0.5
    Restores CSI to [-0.5, 0.5] range in both real and imaginary parts
    Required to correctly analyze magnitude, delay profiles, and angular structure